## Slide 1
CONCEPTUAL DESIGN REPRESENTATION OF AIR DECAY LEAK TEST MACHINE

## Slide 2
Air decay LTM
1)Body leak test
component
LEAK TEST | ABSOLUTE TEST PRESSURE(BAR) | ALLOWABLE LEAK RATE(cm3/min)
BODY | 1 | 3

## Slide 3
H=2000mm
L=900mm
W=500mm
Part Loading H=900mm
Machine Overall Dimensions

## Slide 4
Safety curtains
Operator Console
OPERATOR PENDENT BOX
PC FOR DATA STORAGE & SCADA
Machine Structure
CASTER WHEEL
Electrical & pneumatic panel
REJECTION BIN WITH SENSOR
4 PORT LEAK TESTER TA 04

## Slide 5
LASER GALVO ADJUSTMENT SLIDE
BOTTOM SEALING PLATE
Main Fixture Pillar
Top clamping SWIVEL CYLINDERS
LASER MARKING AREA 200X200
1)Body leak test
PART PRESENCE SENSORS

## Slide 6
Bottom seal plate
c/s
Air inlet ports

## Slide 7
OK PART LASER MARKING FORMAT

## Slide 8
Sequence of operations
Load the all 4 jobs on fixture
Press cycle start on machine
Leakage testing cycle
starts
Laser marking machine starts engrave
The O letter mark on job for ok marking
4 port Techtrust Air Leak Tester
Checks the all 4 jobs at a same time
Techtrust Air leak tester Finds JOB in NOT-OK Condition
JOB will unload by Operator
Operator will pick the JOB and send to rejection Bin
NOT-OK JOB
OK JOB

## Slide 9: THANK YOU